## Slide 1: Lezione 4 Introduction to FPGAs and Xilinx devices
Stefan Cristi Zugravel 20/01/2026

## Slide 2: Early times of digital electronics

## Slide 3: Why programmable ICs?
Producing a Chip costs much more than producing a PCB
Using one Chip on many PCBs increases Number of Chips and reduces Costs per Chip
If a Chip is programmable, it can be used on many PCBs in different situations
Producing one wafer costs ~ 10k€
  Not included manpower to design wafer & packaging
Saving space on a PCB

## Slide 4: What are FPGAs?
Field Programmable Gate Array
Simple:
  Programmable Logic Devices
More detailed:
  Programmable Logic Devices
    With lot of additional function-block (e.g. RAM, DSP)
    Flexible configuration
    Can host microcontroller

## Slide 5: History of Programmable Logic Devices /1
1960s: Fuse Configurable Diode Matrix
  First form of programmable logic
  One-Time Programmable (OTP)
1971: Programmable ROM (PROM)
  Logic functions stored as truth tables
  Still limited flexibility and efficiency
PAL (Programmable Array Logic):
  Fixed AND/OR logic structure
  Programmable interconnections
  OTP technology
256 x 8-bit Static/Dynamic PROM

## Slide 6: History of Programmable Logic Devices /2
1978: PLA (Programmable Logic Array)
  Programmable AND plane, fixed OR plane
  Faster and cheaper than PLA
CPLD (Complex Programmable Logic Device)
  Multiple PAL-like blocks
  In-system programmable
  Configuration retained after power-off
Comparison with other Programmable Logic Devices
PLA has a programmable AND gate array and programmable OR gate array.
PAL has a programmable AND gate array but a fixed OR gate array.
ROM has a fixed AND gate array but programmable OR gate array.
The most noticeable difference between a large CPLD and a small FPGA is the presence of on-chip non-volatile memory in the CPLD, which allows CPLDs to be used for bootloader functions

## Slide 7: History of Programmable Logic Devices /3
1989: First Field Programmable Gate Array (FPGA)
  Configurable Logic Blocks (CLBs)
  Programmable routing fabric
  Massive parallelism
Compared to CPLDs:
  Much higher logic density
  SRAM-based configuration (loaded at startup)
  Ideal for complex systems

## Slide 8: Price point

## Slide 9: Fundamental FPGA components

## Slide 10: Programmable interconnections /1

## Slide 11: Programmable interconnections /2
Programmable Switch Matrix

## Slide 12: Look-up tables (LUT) /1
How to implement a 2-bit truth table (boolean logic) ?
XNOR

## Slide 13: Look-up tables (LUT) /2
FPGA solution: write the truth table into a RAM !

## Slide 14: Look-up tables (LUT) /3

## Slide 15: Logic Cell (LC)
Xilinx terminology :
Logic Cell (LC) = 1x LUT + 1 register (FF) + programmable MUX
LUT implemented as 6-inputs, 64-bit RAM
slice = 4x LUTs + 8 registers (FFs) + MUXs + fast-carry chain (CLA)
Congurable Logic Block (CLB) = 2x slices
Basic Element (BEL) = any device primitive
WHY?
carry-lookahead adder

## Slide 16: Programmable I/O pads
I/O BLOCK
Programmable
pad

## Slide 17: Xilinx FPGA line-up

## Slide 18: Xilinx 7-series family comparison
Different size, number of programmable logic cells, I/O capabilities, performance and cost depending on the chosen device family :
Spartan 7 : lowest-cost, lowest-power, good I/O performance, lowest number of resources
Artix 7 : low-power, medium number of resources and I/O, good choice for DSP
Kintex 7 : best compromise between number of resources, I/O, speed, power and cost
Virtex 7 : highest system performance (resources, speed, I/O) but also largest power consumption and highest cost

## Slide 19: How “programming” a FPGA?
Describe what the hardware should do.
Check Syntax
“compiles” the design to transform HDL source into an architecture-specific design netlist. (connections)
Merges incoming netlists and constraints into a Xilinx design file
→ connections are merged with timing
Fits the design into the available resources
→ tell the FPGA which gate structures should be used
Places and routes the design to the timing constrains
→ decide, which gate is used for which function
Write configuration into the FPGA or configuration memory

## Slide 20: Xilinx XDC – Xilinx Design Constraints file
XDC constraints are based on the standard Synopsys Design Constraints (SDC) format. SDC has been in use and evolving for more than 20 years, making it the most popular and proven format for describing design constraints.

## Slide 21: Recommended Constraints Sequence

## Slide 22: Example: Digilent Arty-A7 evaluation board
Device: Xilinx Artix-7